## Slide 1
PUCSL Solar & Weather Prediction System
Machine Learning-Based Renewable Energy Forecasting for Sri Lanka
Research Project 2026 | Public Utilities Commission of Sri Lanka
15 Years Data (2010-2025) | 1,242 Grid Cells | 475 Real Solar Plants | 4 Prediction Equations

## Slide 2
Project Overview
• Sri Lanka needs accurate renewable energy forecasting for national grid stability
• This system predicts Solar Generation, Temperature & Rainfall for any location
• Entire country covered using a 10km x 10km grid = 1,242 grid cells
• Built using 15 years of historical weather data (2010-2025)
Data Sources:
• OpenMeteo API - reanalysis weather data for all 1,242 grid cells
• 24 official Meteorological Stations (Department of Meteorology, Sri Lanka)
• 475 real solar plants (PUCSL) - 8,201 rows of monthly generation data
Final Output:
• Monthly & annual solar generation (kWh) for any location and installed capacity (kWp)

## Slide 3
Data Pipeline - How It All Flows
• Step 1: Raw weather downloaded from OpenMeteo API -> T_om, RF_om for 1,242 cells
• Step 2: Actual measurements from 24 meteorological stations collected
• Step 3: Error Correction Equations applied -> T_corrected, RF_corrected
• Step 4: Corrected data merged with real solar plant generation records
• Step 5: Machine Learning models trained (Temperature, Rainfall, Solar)
• Step 6: Models applied to all 1,242 grid cells x 12 months = 14,904 predictions
• Step 7: Results visualized on interactive maps and Streamlit dashboard

## Slide 4
What are Beta (B) Coefficients?
• Beta values are the coefficients the model LEARNS from historical training data
• They represent how much each input variable contributes to the prediction
Beta symbols and meaning:
• B0 = Intercept - base value when all inputs equal zero
• B1, B2, B3 ... = Weights assigned to each input variable
Interpreting Beta values:
• Large positive B -> that variable strongly INCREASES the output
• Large negative B -> that variable strongly DECREASES the output
• B close to 0 -> that variable has LITTLE effect on the output
How Beta is calculated - Ordinary Least Squares (OLS):
• Minimize: Sum of ( yi - y_predicted )^2 where yi = actual, y_predicted = predicted

## Slide 5
Why sin(m) and cos(m)? - Cyclical Month Encoding
• Raw month number (1-12) treats December(12) and January(1) as FAR apart numerically
• But December and January are climatically ADJACENT - this causes prediction errors!
Solution: Encode month as sine and cosine to wrap the calendar into a smooth circle:
• month_sin = sin( 2*pi * month / 12 )
• month_cos = cos( 2*pi * month / 12 )
Example values:
• January -> sin = +0.500, cos = +0.866
• July -> sin = -0.500, cos = -0.866
• December -> sin = -0.866, cos = +0.500 (close to January - correct!)
Interaction features also used:
• lat x sin(m), lat x cos(m), lon x sin(m), lon x cos(m), elev x sin(m), elev x cos(m)

## Slide 6
Equation 1 - Temperature Error Correction
Purpose:
• OpenMeteo reanalysis data has systematic bias vs actual ground measurements
• This equation corrects that bias using official met station data
Equation:
• T_corrected = B0 + B1.lat + B2.lon + B3.elev + B4.month + B5.T_om
Input Variables:
• lat = Latitude (degrees N) | lon = Longitude (degrees E)
• elev = Elevation in meters above sea level
• month = Month number (1 = January ... 12 = December)
• T_om = Raw temperature from OpenMeteo (degrees C)
Output: T_corrected = Bias-corrected temperature (degrees C)
• B3 (elevation) is NEGATIVE - higher elevation = cooler temperature
• B5 (T_om) close to 1.0 - OpenMeteo is mostly accurate, small correction needed

## Slide 7
Equation 2 - Rainfall Error Correction
Purpose: Correct OpenMeteo rainfall bias using actual met station measurements
Equation:
• ln(RF_corrected) = B0 + B1.lat + B2.lon + B3.elev + B4.month + B5.ln(RF_om + 1)
Input Variables:
• lat, lon, elev, month = same as temperature equation
• RF_om = Raw rainfall from OpenMeteo (mm)
• ln(RF_om + 1) = Natural log of raw rainfall (+1 added to handle zero-rainfall months)
Output: RF_corrected = Bias-corrected rainfall (mm)
Why log transformation?
• Rainfall is right-skewed - log normalizes the distribution for better accuracy
• +1 inside the log prevents ln(0) which is mathematically undefined

## Slide 8
Temperature Prediction Model - Features & Data
Purpose: Predict monthly temperature for any location and year in Sri Lanka
12 Input Features:
• lat, lon, elevation, month_sin, month_cos, year
• lat x sin(m), lat x cos(m), lon x sin(m), lon x cos(m), elev x sin(m), elev x cos(m)
Training Data:
• 44,047 rows - 207 OpenMeteo grid cells + 24 meteorological stations merged
• Latitude range: 5.96 N to 9.68 N (full Sri Lanka including northern cities)
• Years covered: 2010-2025 (15 years)

## Slide 9
Temperature Model - Results Comparison
R2=0.987 means 98.7% of temperature variance explained | MAE = only 0.18 C average error
Model
R2 Score
MAE
Verdict
Linear Regression
0.8528
0.6799 C
Good
Polynomial (degree 2)
0.9054
0.5341 C
Better
Random Forest BEST
0.9870
0.1769 C
Excellent
Gradient Boosting
0.9619
0.3403 C
Very Good

## Slide 10
Rainfall Prediction Model
Purpose: Predict monthly rainfall for any location and year in Sri Lanka
Same 12 input features as temperature model:
• lat, lon, elevation, month_sin, month_cos, year + 6 interaction features
Best Model: Random Forest - R2 = 0.956
• 95.6% of rainfall variance is explained by the model
Why slightly lower R2 than temperature?
• Rainfall is more spatially variable and event-driven than temperature
• A single storm can cause large local variation hard to capture at grid level
• Nevertheless 95.6% is excellent accuracy for rainfall prediction
Training Data:
• Same 44,047 rows covering full Sri Lanka (5.96 N to 9.68 N)

## Slide 11
Equation 3 - Solar Specific Yield Prediction
Purpose: Predict solar energy per kWp of installed capacity per month
Equation:
• SpecificYield = B0 + B1.lat + B2.lon + B3.elev + B4.sin(m) + B5.cos(m) + B6.T_corrected + B7.RF_corrected
Coefficient Interpretation:
• B1 (lat): NEGATIVE - higher latitude = less solar yield
• B2 (lon): NEGATIVE - moving east = wetter climate = less solar
• B3 (elev): POSITIVE - higher elevation = clearer atmosphere = more solar
• B6 (T): POSITIVE - warmer = more sunshine hours = more solar
• B7 (RF): NEGATIVE - more rain = cloud cover = less solar
Fitted equation from actual training data:
• SpecificYield = 769.26 - 4.20.lat - 8.03.lon + 0.008.elev - 2.07.sin(m) + 1.17.cos(m) + 1.59.T - 8.72.ln(RF)

## Slide 12
Equation 4 - Final Energy Generation Prediction
• Final step: converting specific yield into actual energy generation for a plant
Equation:
• Predicted kWh = Specific Yield (kWh/kWp) x Capacity (kWp)
Worked Example:
• Location: Colombo | Month: February | Installed Capacity: 10 kWp
• Specific Yield predicted by model = 110 kWh/kWp
• Predicted Generation = 110 x 10 = 1,100 kWh for February
• Annual Generation = Sum of all 12 monthly predictions
Why this matters for PUCSL:
• Any plant size can be evaluated - from 5 kWp school rooftop to 1,000 kWp solar farm
• Grid planners can estimate contribution before installation begins

## Slide 13
Solar Generation Model - Results Comparison
Lower R2 expected: solar also depends on panel brand, inverter efficiency, shading, dust - not in dataset
Model
R2 Score
MAE
Notes
Linear Regression (log RF)
0.0799
25.28 kWh/kWp
Baseline
Linear Regression (plain RF)
0.1160
24.46 kWh/kWp
Better
Polynomial Regression deg 2
0.1240
24.38 kWh/kWp
Best - used

## Slide 14
Sri Lanka Solar Potential Mapping - Results
1,242 cells x 12 months = 14,904 predictions | Top: Colombo, Moratuwa | Lowest: Near Mullaitivu
Category
Annual Yield (kWh/kWp)
Grid Cells
Very High
> 1,320
1
High
1,200 - 1,320
226
Medium
1,000 - 1,200
484
Low
< 1,000
345

## Slide 15
Correlation Analysis - Key Findings
These correlations confirm that model features are physically meaningful and correctly chosen
Relationship
r Value
Strength
Physical Meaning
Solar vs Temperature
r = +0.50
Moderate Positive
Warmer -> more sun -> more solar
Solar vs Rainfall
r = -0.71
Strong Negative
More rain -> clouds -> less solar
Temperature vs Rainfall
r = -0.91
Very Strong Negative
Hot dry vs cool wet months

## Slide 16
Streamlit Dashboard - System Features
• A fully interactive web application built with Python Streamlit
Dashboard Modules:
• Home - Project overview, key statistics, institutional summary
• Solar Prediction - Monthly/annual kWh for any city, capacity and year
• Weather Prediction - Monthly temperature and rainfall for any location
• Maps Viewer - Interactive Folium maps: solar, temperature, rainfall across Sri Lanka
• Correlation Analysis - r values between solar, temperature, and rainfall
• Data Visualizations - Spatial distribution charts by district and province
Technical Stack:
• Python | Streamlit | Scikit-learn | Pandas | Folium | Plotly | Joblib

## Slide 17
Key Findings and Contributions
• Complete ML pipeline built for renewable energy prediction across Sri Lanka
Model Performance:
• Temperature model: R2 = 0.987 - near-perfect accuracy (MAE = 0.18 C)
• Rainfall model: R2 = 0.956 - excellent accuracy
• Solar model: Polynomial regression - physically interpretable equation for PUCSL
Coverage:
• All 1,242 grid cells across Sri Lanka mapped with solar potential
• Northern Sri Lanka (Jaffna, Vavuniya, Mannar) correctly predicted with station data
• 15 years of historical data (2010-2025) ensures robust and reliable predictions
Impact:
• PUCSL can now forecast solar contributions before any plant is installed
• Supports national energy transition planning and grid stability management